## Slide 1: HamSCI HF Multipath Propagation Mode Analysis Using Amateur Radios and Audio Waveforms Sensitive to Time Difference of Arrival (TDOA)
Steve Cerwin WA5FRF, Jesse T. McMahan K1FR,
Alexandros Papadopoulos KC3WUD, Gerard Piccini KD2ZHK,
Paul Bilberry N5DUP, Sam Blackshear AB5YO
Kristina V. Collins KD8OXT, Nathaniel A. Frissell W2NAV
American Geophysical Union (AGU) Fall Meeting 2024
December 9-13, 2024
steve@cerwinconsulting.com
Notes: Good morning! My name is Steve Cerwin and I am going to talk about a way of probing the bottom side ionosphere using ordinary amateur radios transmitting and receiving audio waveforms that can reveal the Time Difference of Arrival, or TDOA between multipath propagation modes.

## Slide 2: TDOA Plots with a 2:1 Relationship Observed Over a Near Vertical Incidence Skywave (NVIS) Path
1F2 2F2 3F2
F2 Layer at ~ 290 km
Earth
1F2 - 2F2
TDOA
1F2 - 3F2
TDOA
NVIS Path Where Distance Between Stations is Small Compared to Layer Height
Path 1F2 - 3F2 : DP = 6h - 2h = 4h
Path 1F2 - 2F2 : DP = 4h - 2h = 2h
Path Length for 1F2 - 3F2 is exactly twice
1F2 - 2F2 for NVIS Paths.
The nearly exact doubling in TDOA is theorized to be a result of TDOA between 1-hop and 3-hops from F2.
Both the baseline values and the many of the inflection amplitudes along the plots are doubled.
h
Not to scale
Ground Distance = 8.7 km

## Slide 3: TDOA Plots with a 2:1 Relationship Observed Over a Near Vertical Incidence Skywave (NVIS) Path
Path 1F2 - 2F2 : DP = 4h - 2h = 2h
Path 1F2 - 3F2 : DP = 6h - 2h = 4h
Path Length for 1F2 - 3F2 is exactly twice
1F2 - 2F2 for NVIS Paths where distance between station is small compared to the layer height.
F2 Layer at ~ 290 km
1F2 2F2 3F2
Earth
h
Not to scale