## Slide 1: Simplified 1 and 2 Hop Refraction from The F2 Region
Day ~ 300 km
Night ~ 220 km
UV and X radiation from the sun photoionize the upper atmosphere into free electrons and positively charged ions.
Complex photochemical reactions with oxygen, ozone, nitrogen, and nitrous oxide arrange the ionization into layers labeled D, E, and F (F1 and F2).
Velocity gradients in the ionized layers refract upward directed radio waves back to earth. Multiple hops involving reflection from the earth and other layers are possible, enabling global radio propagation.
Most HF radio propagation comes from the E and F layers. The D layer primarily acts as an attenuator with attenuation increasing with wavelength.
Great Circle Ground Distance
F2 Region
200-330 km
E 100-115
D 60-90
Notes: UV and X radiation from the sun photoionize the upper atmosphere into free electrons and positively charged ions.
Complex photochemical reactions with oxygen, ozone, nitrogen, and nitrous oxide arrange the ionization into layers labeled D, E, and F.
Velocity gradients in the ionized layers refract upward directed radio waves back to earth in the HF frequency range from 3-30 MHz.
Multiple hops involving reflection from the earth and other layers are possible, enabling global radio propagation.
Most HF radio propagation comes from the E and F layers. The D layer primarily acts as an attenuator with attenuation increasing with wavelength.
The F layer changes height significantly with diurnal changes in solar radiation. The E layer does so as well, but to a much smaller degree. The rate of height change imparts velocity on path length which results in Doppler shifts in frequency.
This paper postulates a phenomenology to explain observed complex Doppler behavior, specifically mode splitting, as a function of differential path velocity imparted on single and multiple hop modes by changing layer height.

## Slide 2: Simultaneous 1 Hop Refraction from the E and F2 Regions
Day ~ 300 km
Night ~ 220 km
UV and X radiation from the sun photoionize the upper atmosphere into free electrons and positively charged ions.
Complex photochemical reactions with oxygen, ozone, nitrogen, and nitrous oxide arrange the ionization into layers labeled D, E, and F (F1 and F2).
Velocity gradients in the ionized layers refract upward directed radio waves back to earth. Multiple hops involving reflection from the earth and other layers are possible, enabling global radio propagation.
Most HF radio propagation comes from the E and F layers. The D layer primarily acts as an attenuator with attenuation increasing with wavelength.
Great Circle Ground Distance
F2 Region
200-330 km
E 100-115
D 60-90
Notes: UV and X radiation from the sun photoionize the upper atmosphere into free electrons and positively charged ions.
Complex photochemical reactions with oxygen, ozone, nitrogen, and nitrous oxide arrange the ionization into layers labeled D, E, and F.
Velocity gradients in the ionized layers refract upward directed radio waves back to earth in the HF frequency range from 3-30 MHz.
Multiple hops involving reflection from the earth and other layers are possible, enabling global radio propagation.
Most HF radio propagation comes from the E and F layers. The D layer primarily acts as an attenuator with attenuation increasing with wavelength.
The F layer changes height significantly with diurnal changes in solar radiation. The E layer does so as well, but to a much smaller degree. The rate of height change imparts velocity on path length which results in Doppler shifts in frequency.
This paper postulates a phenomenology to explain observed complex Doppler behavior, specifically mode splitting, as a function of differential path velocity imparted on single and multiple hop modes by changing layer height.

## Slide 3
Computer with .wav Chirp Waveform
Sound
Card
Output
HF
Transmitter
Mic
Input
Interface
Night ~ 300 km
Day ~ 220 km
F2 Region
200-350 km
E 90-120
D 60-90

## Slide 4
Notes: UV and X radiation from the sun photoionize the upper atmosphere into free electrons and positively charged ions.
Complex photochemical reactions with oxygen, ozone, nitrogen, and nitrous oxide arrange the ionization into layers labeled D, E, and F.
Velocity gradients in the ionized layers refract upward directed radio waves back to earth in the HF frequency range from 3-30 MHz.
Multiple hops involving reflection from the earth and other layers are possible, enabling global radio propagation.
Most HF radio propagation comes from the E and F layers. The D layer primarily acts as an attenuator with attenuation increasing with wavelength.
The F layer changes height significantly with diurnal changes in solar radiation. The E layer does so as well, but to a much smaller degree. The rate of height change imparts velocity on path length which results in Doppler shifts in frequency.
This paper postulates a phenomenology to explain observed complex Doppler behavior, specifically mode splitting, as a function of differential path velocity imparted on single and multiple hop modes by changing layer height.

## Slide 5
Computer with .wav Chirp Waveform
Sound Card Output
AM or SSB
HF Transmitter
Mic Input Interface
Computer with .wav Capture Program
Sound Card Input
AM or SSB
HF Receiver
Audio Output
Skywave path with ground distance and operating frequency suitable for multi-hop propagation.

## Slide 6
Computer with .wav Chirp Waveform
Sound Card Output
WA5FRF SSB
HF Transmitter Near San Antonio, TX
Mic Input Interface
Computer with .wav Capture Program
Sound Card Input
N5DUP SSB
HF Receiver Near Abilene, TX
Audio Output
Skywave path with ground distance and operating frequency suitable for multi-hop propagation.
Frequencies for initial tests: 3.780 and 5.3715 MHz
Ground Distance = 317 km